CWSPARAM                provided by Charles W Sandmann (sandmann@clio.rice.edu)
                                    102 Hurst Ct, Destrehan, LA 70047
CWSPARAM OVERVIEW

There are certain parameters built into the CWSDPMI.EXE and CWSDPR0.EXE images
which might need to be modified for distributing some programs for better 
performance.  The modified image could be renamed, and then the DPMI server
name in a DJGPP V2 image may be stubedited to use the new name.  The parameters
which can be modified are discussed below:

Full name of paging file ("" to disable) ? [c:\cwsdpmi.swp]

 This is where the file which provides virtual memory should be located.  It
 may be desirable to change the default to a faster disk or one with more
 free space.  To disable paging, enter two double quotes.  The file name
 MUST contain the disk, full path, and file name.  Anything less may cause
 unpredictable behavior.  Press return to keep the current value.

Number of page tables to initially allocate (0=auto) ? [0]

 Page tables are stored in the DOS memory area and consume this precious
 resource.  The default value of 0 chooses automatic allocation of enough
 page tables to hold all of the physical memory without paging (with the 
 minimum enough to hold 20Mb without paging).  If your program is a fixed
 size (and does not spawn any other DPMI images) you can specify one page
 table for each 4Mb of your program's size.  If your program is small, this
 can save a small amount of DOS memory, which might be needed for other
 purposes.  If your program is large (typically larger than the physical
 memory) specifying a number will consume more DOS memory but improve 
 performance since the page tables themselves will not page.  CWSDPMI will
 attempt to dynamically allocate additional page tables at run time to 
 prevent paging, but if all of the DOS memory is free, performance would
 be degraded.  Remember to add an extra page table if mapping physical devices.

Minimum application memory desired before 640K paging ? [256Kb]

 Typically, CWSDPMI only uses extended memory to return as DPMI memory, and
 saves the DOS memory area for DOS requests.  On small memory machines with
 applications not needing much DOS memory (or poorly tuned memory management)
 there may be very little extended memory left available, with up to 600K of
 DOS memory unused.  This parameter determines the threshold which CWSDPMI
 should start using DOS memory as DPMI memory.  If an application is known to
 not need much DOS memory, this value could be set to the size of the memory
 required for the image, which provides roughly 0.5Mb additional memory before
 paging happens.  This parameter is one I would expect might be adjusted when
 distributing an application for maximum performance on a wide variety of
 machines.

Paragraphs of DOS memory to reserve when 640K paging ? [3840]

 If the image needs to page in the DOS memory area (triggered by the parameter
 value above), this parameter tells how much DOS memory to save for DOS 
 allocation requests.  The value is in paragraphs (16 byte increments), so the
 default is 60Kbytes.  You will actually end up with a bit more probably, since
 the page tables are allocated on 4Kbyte rounded boundaries.  Some amount of
 DOS memory needs to be saved for potentially expanding the file table, the
 sbrk() algorithm, DMA buffers, etc.  This amount can be tuned on an image
 by image basis, and may be as little as 0.